## Slide 1: Measurements of Nucleon Removal Cross Sections for 90Sr with a Thick Solid Deuterium Target
2026/08/24
Degree Programs in Pure and Applied Sciences
University of Tsukuba
Hayato Kobayashi
Notes: The title of my presentation is “[Title].” My name is Hayato Kobayashi from the University of Tsukuba.

## Slide 2: Neutron Skin and Reaction Cross Section σR
the neuton distribution radii
in a nucleus.
Neutron skin thickness
the proton distribution radii
in a nucleus
Δr ∝ param.L of EoS
密度分布の、グラフの絵にすると
π()2
Projectile
Target
Area of a circle
σR and Nuclear Radii Assuming a Uniform Nucleon Density Distribution (Black-Sphere Model)
the neuton density distribution
the proton density distribution
density ρ
Distance from the center r
σR : the probability of nuclear reaction
(except for elastic scattering)
Include information of nuclear radii
Short life time ＆ rare RI
σR ⇒ Δr
Notes: We aim to determine neutron skin thickness of neutron-rich nuclei using reaction cross section measurement.
Neutron skin thickness (Δr)is defined the difference between the neuton distribution radii(rn) and the proton distribution radii(rp) in a nucleus.
The magnitude of Δr is related to the stability of pure neutron matter as slope parameter L near nuclear density.
Reaction cross section(σR) represents the probability of nuclear reactions occurring and is sensitive to the nuclear radius.
In a simple picture, we assume that a reaction occurs when the projectile comes into contact with the target nucleus.
The larger the nuclear radius, the higher the probability of contact.
In addition, reaction cross-section measurements use the nuclei of interest as RI beams, allowing us to measure even short-lived and difficult-to-produce unstable nuclei.
For determining the neutron skin thickness, reaction cross-section measurements are expected an effective method.
In generally, The more neutron-rich the nucleus is, the larger its neutron skin thickness becomes, making it more sensitive to L. Therefore, we aim to determine the neutron skin thickness of neutron-rich nuclei.

## Slide 3: Derivation of Δr by σR measurements
https://pdg.lbl.gov/2019/hadronic-xsections/hadron.html
rn ⇒ Proton Tgt. (sensitive to rn)
rp ⇒ Neutron Tgt. (sensitive to rp)
Exp.
(Deuterium)
exp.
(Hydrogen [1])
calc.
derivation
W.Horiuchi et al. PRC, Vol. 102, p. 054601, 2020.
Projectile
nuclei
Proton
Target
nuclei
Derivation method of for neutron Tgt.
Eclipse
Deuteron
Merit of the Solid Deuterium Target (SDT)
Pure Deuteron Target ⇒ high measurement accuracy
High Density ⇒ high reaction rate
[1] T. Moriguchi et al. / Nuclear Instruments and
Methods in Physics Research A 624 (2010) 27–32
: σR for proton (neutron, deuteron) tgt.
the neuton distribution radii
in a nucleus.
Neutron skin thickness
the proton distribution radii
in a nucleus
Notes: I will explain the Derivation of Δr by σR measurements.
According to the isospin asymmetry of nucleon-nucleon total cross section, rn is sensitive to proton target and rp is sensitive to neutron target at several hundred MeV.
So, we want to conduct reaction cross section measurement using proton and neutron target.
However, preparation of pure neutron target is not feasible.
Theoretical studies suggest that the reaction cross section for a neutron target can be derived from measurements using proton and deuteron targets.
Therefore, we are developing the solid deuterium target (SDT) for reaction cross section measurement as deuteron target.
For its development, we are using the existing solid hydrogen target production system as a basis.

## Slide 4: Solid Deuterium Target (SDT)
vacuum chamber
D2 gas handler
He gas handler
Kapton films
In the experiment
lifting system
beam
50 mm
Notes: This is what the solid deuterium target (SDT) production system looks like. (Click)
This is the beam irradiation section. One of its key features is that we can switch between Tgt in and Tgt out using a lifting system, without melting the SDT.

## Slide 5: Fabrication of SDT
~ 300 K
500 ~ 200 torr
(tank pressure)
~ 300K
180 torr
10K
180 torr
Flow Room-temperature D2 gas
Control D2 gas pressure : 180 torr
Control Cell temperature : 10 K
15 min
60 min
Fabrication (~ 90 min)
Gradually increase the cell temperature
The gas flows back due to the pressure difference
Recovery (~ 40 min)
beam
Successfully solidified
86 min (complete)
No beam irradiation test yet
Notes: I will explain how the SDT is fabricated.
The SDT is fabricated by flowing room-temperature deuterium gas into the cooling cell.
The fabrication procedure is as follows.
First, we flow room-temperature deuterium gas into the cell.
Second, we control the gas pressure at 180 torr using a pressure control system.
Finally, we control the cell temperature at 10 K using a cryostat and a heater.
It typically takes about 1.5 hour to complete the solidification of deuterium in the cell.
Here, you can see the fabrication process over time.
We have successfully achieved solidification of deuterium.
For recovery, we gradually increase the cell temperature using the heater. The deuterium gas then flows back due to the pressure difference.
The typical recovery efficiency is about 99%.(680 mbar ⇒ 675 mbar)
As the current status, no beam irradiation test has been conducted yet.

## Slide 6: Purpose of the study
[2] H. Wang, et al., Phys. Lett.B 754,104(2016).
Conduct a beam irradiation experiment and evaluate feasibility of the SDT for cross-section measurements
Nucleon-removal cross section σ-xN
Measured already at RIKEN RIBF [2]
90Sr + H, 2H (185 MeV/u)
Target : CD2, CH2, C
Purpose
Method
Nucleon-removal
cross section [mb]
Notes: Our reserch objective is to conduct a beam irradiation experiment and evaluate feasibility of the SDT for cross-section measurements.
To evaluate the SDT, We measure the nucleon-removal cross sections of a 90Sr and compare with the previous data.
because nucleon-removal cross section for 90Sr on D was previously measured using CD2 and C.

## Slide 7: Nucleon Removal Cross Section σ-xN
SDT thickness
proton
90Sr
counts
89Rb
counts
detectors
detectors
90Sr
①
②
: counts of produced nuclei w/ (w/o) Tgt.
: counts of projectile nuclei w/ (w/o) Tgt.
: one proton removal cross section
: thickness of Tgt.
’: reaction cross section for produced nuclei
: reaction cross section for projectile nuclei
Transmission method
In the case of one proton removal (90Sr→89Rb)
Notes: I will explain Nucleon Removal Cross Section.
For example, We assume the case where one proton removals and projectile is 90Sr.
In the case of it, produced nuclei is 89Rb.
Basically, we assume that only one reaction occurs, and ⁹⁰Sr is detected as ⁸⁹Rb, and one proton removal cross section is simply written as this.
For a thick target, we need to consider two additional corrections.

## Slide 8: Nucleon Removal Cross Section σ-xN
SDT thickness
proton
90Sr
counts
89Rb
counts
detectors
detectors
90Sr
①
②
: counts of produced nuclei w/ (w/o) Tgt.
: counts of projectile nuclei w/ (w/o) Tgt.
: one proton removal cross section
: thickness of Tgt.
: reaction cross section for projectile nuclei
’: reaction cross section for produced nuclei
Transmission method
In the case of one proton removal (90Sr→89Rb)
Notes: The first is the contribution from secondary reactions: the produced ⁸⁹Rb undergoes another reaction and is therefore not detected as ⁸⁹Rb. The second is the decrease in the number of projectile nuclei as they pass through the thick target.
Considering these factors, one proton removal cross section is written as this.
As corrected factor, Reaction cross sections of projectile and produced nuclei are both measured using transmission method.

## Slide 9: Experiment @ RIKEN-RIBF
Beam production
in-flight fission of a 238U primary beam at 345 MeV/u
Upstream
~ 58 m
Downstream
~ 36 m
Upstream
Downstream
SDT
Notes: Beam irradiation experiment was conducted at the BigRIPS and ZeroDegree beamline of RIKEN RIBF.
A primary 238U beam at 345 MeV/u was incident on a 9Be production target to produce a cocktail beam that included 90Sr via projectile-fission reactions.
The secondary beam was irradiated onto the SDT.
The beam particles were identified on an event-by-event basis using the detectors.

## Slide 10: Particle Identification (PI)
TOF-Bρ-⊿E method
✓TOF (Time of Flight) ⇒ velocity
✓Bρ (magnetic rigidity) ＆ TOF ⇒ A/Q
✓⊿E (energy loss) ＆ TOF⇒ Z
A : Mass number
Q : Charge number
Z : Atomic number
Pla
Pla
IC
TOF
Magnetic Field
B
Radius of curvature
ρ
Energy loss ⊿E
PPAC
PPAC
Z
A/Q
Notes: The particles were identified using the TOF–Bρ–ΔE method.
Two plastic scintillation counters were used to measure the time of flight and determine the particle velocity.
A dipole magnet and position detectors were used to measure the magnetic rigidity.
An ionization chamber was used to measure the energy loss of the particles.
From the Lorentz force, we can derive the mass-to-charge ratio A/Q by combining the magnetic rigidity and the velocity.
Using the Bethe–Bloch equation, we can determine the Atomic number Z by combining the energy loss and the velocity.
In this way, we can identify the particles on an event-by-event basis.

## Slide 11
90Sr38+
89Rb37+
90Sr38+
90Sr37+
89Rb37+
89Rb36+
89Rb37+
Downstream PI
(90Sr is selected)
(89Rb is selected)
: counts of produced nuclei w/ (w/o) Tgt.
: counts of projectile nuclei w/ (w/o) Tgt.
: Nucleon removal cross section
: reaction cross section for produced nuclei
: reaction cross section for projectile nuclei
: thickness of Tgt.
σ-xN Analysis
Z
A/Q
Z
A/Q
Z
A/Q
90Sr
①
②
SDT
Notes: The particles downstream of the SDT were also identified using the TOF–Bρ–ΔE method.
I will explain how we derive the nucleon-removal cross section, taking one-proton removal as an example.
First, we can determine the reaction rate by comparing the number of 90Sr particles upstream with the number of 89Rb particles downstream.
Second, we can determine the reaction cross section of the produced nucleus, 89Rb, by comparing the 89Rb yields upstream and downstream.
Similarly, we can determine the reaction cross section of the projectile, 90Sr, by comparing the 90Sr yields upstream and downstream.
In addition, to correct for reactions occurring in the detectors, we performed the same measurement without the SDT.

## Slide 12: Result of σ-xN and Discussion
Preliminary
H. Wang, et al., Phys. Lett.B754,104(2016).
SDT-based measurements are consistent
with existing ⁹⁰Sr + ²H data with CD2 and C
⇒ Cross-section measurements using SDT are feasible!
90Sr+2H
Notes: This is the result.
Red plots are present SDT-based data.
Black ones are previous data using CD2 and C target.
The results are in good agreement with the previous measurements, demonstrating that reaction cross-section measurements using the developed SDT are feasible.

## Slide 13: Summary and Outlook
Summary
・Reaction cross section measurements for proton and deuteron target
are expected to effective method for determining neutron skin thickness.
・We conducted a beam irradiation experiment to evaluate the
the SDT system.
・The SDT-based nucleon removal cross sections are in agreement
with previous data obtained CD2 and C targets within error.
⇒Feasibility of the SDT for σR measurements was confirmed.
Outlook
・Establish a method to measure neutron skin thickness using proton and
deuteron targets (ex. 132Sn) for a precision determination of L in EoS.
Notes: 展望 : SDTで物理実験をしたい。
他手法、陽子弾性散乱(proton elastic scattering)、アルファ粒子弾性散乱、双極子共鳴(dipole magnetic resonance)など
In summary, The SDT production system was successfully validated through the measurement of nucleon-removal cross sections. Next, we aim to demonstrate the method by measuring the neutron skin thickness using reaction cross sections with proton and deuteron targets.

## Slide 14: Collaborators
1. University of Tsukuba
2. RIKEN Nishina Center
3. Tokyo City University
4. Kyushu University
5. Niigata University,
6. The University of Osaka
7. Saitama University
8. RCNP, The University of Osaka
Hayato Kobayashi¹,², Tetsuaki Moriguchi¹,², Akira Ozawa¹,², Daiki Nishimura³,², Masaomi Tanaka⁴,², Miki Fukutome⁵,², Soshi Ishitani⁶,², Ryo Taguchi⁶,², Gen Takayama⁶,², Asahi Yano¹,²,
Kazuhiro Adachi⁵,², Hidetada Baba², Shun Endo³,², Mitsunori Fukuda⁶,², Naoki Fukuda², Yi He³,², Yuto Ichinohe², Chinami Inoue³,², Rinon Kageyama³,², Yuta Kikuchi⁷,²,Nobuyuki Kobayashi⁸, Kensuke Kusaka², Keita Maeda³,², Kento Matsuyama³,², Shin'Ichiro Michimasa²,
Mototsugu Mihara⁶,², Misaki Mikawa¹,², Maoto Mitsui¹,², Daisuke Nagae⁷,², Satoru Nishizawa⁷,², Masao Ohtake², Takashi Ohtsubo⁵,², Claudio Santonastaso², Rena Sasamori⁵,², Fubuki Sato³,², Toshiya Shimamura⁵,², Yohei Shimizu², Hiroshi Suzuki²,Takeshi Suzuki⁷,², Hiroyuki Takeda², Shoko Takeshige², Koki Tezuka⁵,², Yasuhiro Togano², Kohei Watanabe⁷,², Takayuki Yamaguchi⁷,², Yoshiyuki Yanagisawa²,Keigo Yasuda⁶,², Ibuki Yasuda⁷,², Masahiro Yoshimoto², Wei Yu⁷,²

## Slide 15: Backup

## Slide 16: w/o Thickness effect
Preliminary

## Slide 17: w/ Energy corr.
Using Modified EPAX2
X.H. Zhang / Nuclear Physics A 915 (2013) 59–69
Preliminary

## Slide 18: Reaction Cross Sections
Preliminary

## Slide 19: Solid Deuterium Target (SDT)
vacuum chamber
D2 gas handler
He gas handler
Kapton films
In the experiment
lifting system
beam
beam
cupper
D2 180 Torr
He 180 torr
He 180 torr
Mylar films
(25μm)
He gas cell
Kapton films
(25μm)
SDT
50 mm
Notes: This is what the solid deuterium target (SDT) production system looks like. (Click)
This is the beam irradiation section. One of its key features is that we can switch between Tgt in and Tgt out using a lifting mechanism, without melting the SDT.
The SDT is produced by flowing deuterium gas into the cell. During the production process, the Kapton windows tend to bulge due to the gas pressure. To suppress this bulging, we attach He cells from the outside to support the Kapton windows.

## Slide 20: 固体重水素標的 (SDT)
実験に使用したSDT
クラック
50mmφ
ビーム
JOURNAL OF RESEARCH of the
National Bureau of Standards
Vol. 89, No.3, May-June 1984
後日、筑波大学で同条件で作成し、
表面のレーザー測定結果 ⇒ SDTの中心厚さ 51.3 ± 0.2 mm
加重平均より
19.9 ± 0.1 cm3/mol
10 K
固体水素での系統誤差
評価方法
核子剥離断面積を導出し、CD2標的(とC標的)を用いた先行研究 [2]と比較する
[2] H. Wang, et al., Phys. Lett.B754,104(2016).
目的や課題を書く
バックアップ
↓
Notes: 作成したSDTはこのようになっております。評価方法として、ビーム照射実験を行い、核子剥離断面積を導出し、リファレンスとの一致をみるということを行いました。
その際、厚さは次のように仮定しました。
モル体積については、温度計が10 Kであったことから、10K付近の文献値を参照しました。
長さについては、後日、同条件で作成し、膜表面の膨らみ測定を1回行ったところ、SDT中心で1.3 mm膨らんでいる可能性がありました。
また、誤差としては、固体水素では複数回の膨らみ測定を過去に行っており、その値で系統誤差を付けました。

## Slide 21: He供給圧力最適化時の、SHT膜厚の系統誤差
~ 0.2 mm

## Slide 22: Feed Back System for suppressing membrane bulging

## Slide 23: BackUp SDTへのビーム入射位置(上流)
89Sr
90Sr
89Rb
88Rb
87Rb
86Kr
85Kr

## Slide 24: BackUp SDTへのビーム入射位置(上流) emt. Cut (Used for analysis)
89Sr
90Sr
89Rb
88Rb
87Rb
86Kr
85Kr

## Slide 25: the bump in the lower right
Slew walkして、tofが大きくなる(βが小さくなる)とすると、
A/Q ⇒ ∝ 1/βなので大きくなる
Z ⇒ ∝β^2なので小さくなる

## Slide 26: PPAC 240 mm

## Slide 27
=()()
であればテーラー展開して、
の発散を防げる

## Slide 28
90Sr38+
89Sr38+
89Rb37+
88Rb37+
87Rb37+
86Kr36+
85Kr36+
92Y39+
PHYSICAL REVIEW C 79,064318 (2009)

## Slide 29: 下流PI
Downstream PI
(90Sr is selected)
(89Sr is selected)
(89Rb is selected)
(88Rb is selected)
(87Rb is selected)
(86Kr is selected)
(85Kr is selected)
90Sr38+
90Sr37+
89Sr38+
89Rb37+
88Rb37+
87Rb37+
85Kr36+
86Kr36+
89Sr38+
89Sr37+
89Rb37+
89Rb36+
88Rb37+
88Rb36+
87Rb37+
87Rb36+
86Kr36+
86Kr35+
85Kr36+
85Kr35+
全核種見せる必要はないので、
これは省く
(バックアっぷ)
Notes: SDT下流の粒子識別も、同様にTOF-Bρ-dE法により行われました。
それぞれの粒子識別図では、SDT上流でどの核種であったかという制限をかけています。
双極磁石への入射段階で、電子が剥がれて、質量電荷比が変化しているイベントも、原子核としては同一粒子として計数しました。

## Slide 30: HL/FS (For Transmission event)
透過イベントのHL/FS比 =反応イベントのHL/FS比
と仮定して
σ-Nは0.9 ~1.4%増加
⇒誤差は4.7%~ついているので、一旦無視

## Slide 31
https://doi.org/10.48550/arXiv.2312.15434
X. Roca-Maza, M. Centelles, X. Vi˜nas et al., Phys. Rev. Lett. 106, 252501 (2011).

## Slide 32
6/9 7:41
6/9 7:58
6/9 8:23
32
SDT used for experiment
crack
50mmφ
ビーム
10 K

## Slide 33
90Sr
counts
90Sr
counts
detectors
detectors
89Rb
counts
89Rb
counts
detectors
detectors

## Slide 35
Deuteron
gas
300 L
tank
Chiller
He Compressor
Cryostat
Tgt.
Cell
pressure
controller
Gas recovery
balloon
Thermal radiation shield
Pressure control valve
Pressure Gauge