## Slide 1
Broadband Lumped-Element Josephson Parametric Amplifier for Axion Search
Uchaikin Sergey for Quantum Sensing Team
IBS/Dark Matter Axion Group
2026-04-23
Notes: Introduction to axion dark matter and the challenges of detection. Emphasize the importance of GHz-range haloscope and noise requirements.

## Slide 2
Introduction
Axion Dark Matter
A promising candidate to explain the universe's missing mass and CP violation.
DMAG’s Challenge
Detecting extremely weak signals across a vast frequency range (our goal: 1-6 GHz).
Notes: Explain the challenge: our FD-JPA in 2020 only covered 30 MHz. Need to match cavity range with amplifier range.

## Slide 3
Axion Haloscope Detection Principle
Magnetic Field
Strong field creates conversion environment (in DMAG 8, 8, 12 and 12 Tesla) .
Axion Conversion
Axions convert to photons in cavity (Q is in the range of 30000_300000).
Signal Detection
Low-noise systems capture faint photon signals (noise is a few unit of the QNL).
Frequency range dictated by axion mass uncertainty.
DMAG/IBS
Notes: Overview of axion haloscope principle: magnetic field, photon conversion in the cavity, quantum-limited detection.

## Slide 4
Optimal read-out:
TWJPA or Flux-Driven JPA?
DMAG/IBS
Cavity for 1-6 GHz range
Tuning cavity range up to 300 MHz
Wideband Detection Challenge
Need to fit amplifier band or tuning range with cavity range >300 MHz

## Slide 5
Broadband Amplification vs Narrowband Axion Signal
Mismatch of bandwidth
Axion signal: ultra-narrowband
TWPA: broadband amplification =>
Excess noise integration
Noise ∝ Δf
Signal occupies tiny fraction of band👉 SNR degrades
Dynamic range problem
Weak signal + large broadband noise
Requires:
  high linearity
  large dynamic range👉 Risk of gain compression
Impact
Reduced sensitivity 👉 Inefficient scanning
Broadband amplifiers are not optimal for👉 detecting narrowband axion signals

## Slide 6
TWJPA: Gain Non‑Uniformity Problem
https://doi.org/10.1103/PhysRevApplied.23.024063
DMAG/IBS
1) Gain strongly varies across frequency (ripple due to multi‑cell line & mismatch)
2) Response depends on pump power
Axion scan requires ultra‑flat response with ~5–10 kHz step
⇒ Gain ripple → non‑uniform sensitivity across scan
https://doi.org/10.1038/nphys2356

## Slide 7
TWJPA: Noise Fluctuations Limit
https://doi.org/10.1103/PhysRevApplied.23.024063
DMAG/IBS
Added noise fluctuates across band; deviates from quantum limit
Origin:
long transmission line
impedance mismatch
System noise inherits this structure
⇒
Frequency‑dependent sensitivity,
slower and less reliable axion scan

## Slide 8
1) To get parametric amplifier a nonlinear element:
The nonlinear current-dependent inductance of a Josephson junction
Flux-driven Josephson Parametric Amplifiers (JPA)
2) To tune frequency:
Average inductance of a SQUID depends from flux bias Φ
Ic –critical current of the SQUID,
Φ0 – flux quantum, 2.069*10^(-15) Wb
I – persistent current, created by dc flux
DMAG/IBS
Notes: How FD-JPA works: non-linear inductance, tuning via flux bias. Show equation and mention limitations.

## Slide 9
Multi-JPA Systems – Gorynych Set
Three JPAs
Combined in parallel in single read-out line.
Frequency multiplexing
JPA is selected by chose of pump frequency fPUMP,
fPUMP~ fSIGNAL.
Six JPAs
Parallel/series arrangements for optimal performance.
Performance
300 MHz bandwidth without noise penalty.
237 MHz
300 MHz
DMAG/IBS
Notes: Gorynych set: 3 JPAs in parallel. 6 JPA combination with parallel/series config. Achieved ~300 MHz bandwidth.

## Slide 10
Lumped Element JPA (Lump JPA)
Design
Discrete components replace distributed elements.
No transmiting line is necessary
Need big interdigital capacitance.
Need higher inductance - a 5-10 SQUIDs in Series
Enhanced Tunability
No transmition line → Wider frequency range accessible with single device.
Reduced need for multiple amplifiers.
Integration
No change in TF line is necessary
DC flux bias need higher current → need some change in next design
DMAG/IBS
Notes: Lumped-element JPA concept: no transmission line. Requires high inductance and interdigital capacitor. Better tunability.

## Slide 11
LJPA Noise Measurements
Noise compare with Quantum Noise Limit (QNL)
One frequency point noise
JPA Gain ~20 dB
In 3-4 GHz range
DMAG/IBS
Notes: Noise measurement of Lump JPA: compares well with QNL. Bias heating issues below 2 GHz.

## Slide 12
Resonance shift because of Flux trapping
ZFC
FC
DMAG/IBS
ZFC method allows extending tuning range of L-JPA

## Slide 13
Flux trapping => Persistent current
ZFC
DMAG/IBS

## Slide 14
Further Tunable Range Enhance by Flux trapping
Zero Field Cooling (ZFC)
4.1-4.7 GHz
DMAG/IBS
6 JPA assembly 300 MHz
3 JPA assembly 150 MHz
1 modified JPA 60 MHz
1 old JPA 30 MHz
Field Cooling (FC)
3.5-4.2 GHz
ZFC method allow increasing useful tuning range from 0.6 to 1.2 GHz
Notes: Characterization of Lump JPA: 1.6 GHz tuning, to compare I show band of our previous read-out. On the right picture is the gain paramap, a dependence of the gain from pump power and pump frequency. Within this border the gain exceed 20 dB.

## Slide 15
Summary
For axion search flux-driven JPA are preferable for read-out because provide more smooth gain and noise characteristics in the frequency band
We can enlarge tuning range of the JPA using field cooling
DMAG/IBS

## Slide 16
Quantum Sensing Team
Sergey Uchaykin
Boris Ivanov
Saebyeok Ahn
Minsu Ko
Seonjeong Oh
Pallavi Parashar
In collaboration with Riken, U. of Tokyo
Yasunobu Nakamura
Chih-Chiao Hung
Arjan F. van Loo
CI – SungWoo Youn
DMAG/IBS

## Slide 17
Read-out Chain Overview
Cavity
Resonant structure where axion-photon conversion occurs.
Amplifier (JPA)
Quantum-limited signal boosting.
Heterodyne Receiver
Frequency conversion and filtering.
DAQ
Data acquisition and analysis.
DMAG/IBS
Notes: Describe the read-out chain: cavity, JPA, heterodyne receiver, DAQ. Emphasize noise and matching importance.

## Slide 18
LJPA Characterization
Tuning with dc flux bias
~1620 MHz,
Gain Paramap
Gain vs (fPUMP,fDETUNING)
DMAG/IBS
Notes: Characterization of Lump JPA: 1.6 GHz tuning, to compare I show band of our previous read-out. On the right picture is the gain paramap, a dependence of the gain from pump power and pump frequency. Within this border the gain exceed 20 dB.