## Slide 1: Thoughts about high Ql operation
TTC 2025
Julien Branlard
Daejeon, 8.4.2025

## Slide 2: Why is bandwidth and resonance control crucial for efficiency
Operating at higher Qext (narrower bandwidth)
  reduces the power needs IF resonance control can be guaranteed
  makes resonance control extremely challenging
Bandwidth (Qext) and Resonance (f) control
Parameters for SRF gun
r/Q = 208 Ohm Vacc = 5 MV (energy gain from the gun at 50 MV/m -> 5 MeV) Ib = 100 uA (100 pC at 1 MHz)
b = 0 deg.
4 kW
Qext = 1e7
Qext = 4e7
1 kW
1.3 kW
2 kW
3.3 kW
The challenge is to find the highest Qext one can operate the cavity at while still meeting the resonance control goals and without compromising operability and reliability of the system.

## Slide 3: Why operating at high Qext ?
Improve RF-to-beam efficiency by reducing the input power needs
It really pays off if resonance control works
i.e. don’t need a huge RF budget for resonance control  piezo
Motivation
Courtesy A. Bellandi

## Slide 4: Challenges at high Qext
Microphonics control
Ponderomotive drops / oscillations
Pulsed operation (transients)
High gradient (LFD)
Courtesy A. Bellandi

## Slide 5: Challenges at high Qext
Ponderomotive drops / oscillations
Ponderomotive drops
Lorentz Force Detuning constant
Cavity half-bandwidth
Cavity voltage
For TESLA cavities, ponderomotive drops start occuring when this ratio becomes smaller than -1.54
Courtesy A. Bellandi

## Slide 6: Challenges at high Qext
Ponderomotive drops / oscillations
Ponderomotive drops
Courtesy A. Bellandi
 |  | Burst (now) | HDC (upgrade)
Qext | x10^6 | 4,6 | 60
f0 | GHz | 1,3 | 1,3
f1/2 | Hz | 0 | 0
Klfd | Hz/MV^2 | -0,9 | -0,9
Vcav | MV | 25 | 20
KlfdVcav^2 / f/12 |  | -4,0 | -33,2

## Slide 7: Challenges at high Qext
IDEA: emulate SEL in pulsed operation during fill
  Rotate common RF phase drive
  Absorb Klfd differences using piezo
Vector sum operation
Courtesy B. Richteri

## Slide 8: Questions
At what Qext are the cavities set to ? (facilities / test stand)
How is Qext set ?
Is it remote controllable ?
How much does it change with operation (thermal effect) ?
Qext

## Slide 9: Questions
What is the level of background microphonics ?
Is there detuning control ?
how ?
Contribution slow tuner / fast tuners ?
Detuning

## Slide 10: Questions
Who is using SEL to drive cavities ?
  at what gradient ?
  SELAP ?
  analogue / digital ?
  Visualization tools ? “Cheeto”
Experience with operating high Qext cavities
  in pulsed mode ?
  in vector sum ?
Experience with ponderomotive drop ?
  At what gradient / Qext
  Frequency of drops
  Recovery time ? How is it handled wrt. to beam operation

## Slide 11: Discussion
Facility | Cavity f0 | Qext [x1e6] | Voltage [MV/m] | Klfd [Hz/MV^2] | CW / pulsed | Field Control | Resonance control
EuXFEL (pulsed) | TESLA 1.3 GHz | 4.6 | 23 | -0.9 | pulsed | VS | Piezo FB
EuXFEL (HDC) | TESLA 1.3 GHz | 6 | 18 | -0.9 | CW pulsed | single | Piezo FB

## Slide 13: BACKUP

## Slide 14: Quench movie